ROTOR BRAKE INSTALLATION INSTRUCTIONS

- The rivet heads on the ring gear must be filed or ground flush with the ring gear bottom.

- Check to determine that the brake will fit between the torque tube and the ring gear with at least 1/32” (.8mm) of clearance. If this clearance does not exist, sand the pad to achieve the required clearance.

- Some rotorheads have holes pre-drilled for the CalumetAir / Wunderlich rotor brake.

- Bensen style head: Remove the forward 3/16” bolt from the torque tube assembly. This will be replaced with a longer bolt.

- Rotorheads with a torque tube not pre-drilled: Clamp the brake to the gear in the correct position. Position the washers as spacers to center the brake on the torque tube. Check to see that the brake handles are parallel with the torque tube with equal space on each side. If possible, transfer punch the torque tube and drill a 3/16” hole with a drill press. You may wish to drill through with a smaller drill from each side and then open the hole to 3/16”.

- Install the pivot bolt, washers and castle nut. Do not over tighten. All parts must pivot freely. Install the cotter pin.

- Check the control stick movement to insure the brake does not impair control range.

- Position the brake actuator bumper against the roll pivot bolt tower. Tilt the rotorhead forward; the brake pad should bear against the ring gear.

- The brake should be engaged gently but firmly the first few times to allow the pad to seat.

Some users have reported that they add washers to the actuator bumper pivot and tighten the assembly to lock the actuator bumper in the engaged position.

By trimming the actuator bumper to the correct length, the actuator bumper becomes the forward rotorhead tilt stop. This makes applying the rotor brake as simple as tilting the rotorhead to the forward most position. Use caution if employing this method.

If you fly enough to wear out the brake pad, return it to us, postpaid, for the free re-bonding of a new pad.  Fly smart, fly safe !