ROTOR TACHOMETER INSTALLATION INSTRUCTIONS

Using the cushion clamp provided, mount the Rotor Tach Sending Unit (RTSU) under the bolt holding the prerotator upper unit to the torque tube as pictured in the photos.

Set the gap between the ring gear teeth and the RTSU to approximately  .005 - .010 of an inch. Larger gaps will work. Test before mounting rotor blades.

Mount Rotor Tach Display Unit (RTDU) where it can be easily seen by the pilot.

Wire the RTSU to the RTDU by attaching the two wires to the two screws on the back (left side) of the display. Silver wire is the shield (ground this to airframe). White wire is the input, attach to input screw. Black wire is also ground, attach to ground screw on back of display.

CalumetAir  Inc.                                             Phone & fax: (708) 895-0398

Web Site: calumetair.com                                 e-mail: gyroplanes@aol.com

Vers 1.0     Desktop/Wunderlichs/Business/instructions.doc

# Text boxes

INPUT (WHITE)

GROUND (BLACK)

SILVER (SHIELD)

DISPLAY UNIT